## Slide 1: Unit – 3 Logic Function Realization with MSI Circuits
Hardik Doshi
 99789 11553
 hardik.doshi@darshan.ac.in
Digital Electronics (2131004) Darshan Institute of Engineering & Technology

## Slide 2: Topics to be covered
Combinational Logic with Multiplexers and Decoders
Standard Logic Functions with MSI Circuits
Design Problem Using MSI Circuits.

## Slide 3: Half Adder
A combinational circuit which adds two one-bit binary numbers is called a half-adder.
The sum column resembles like an output of the XOR gate.
The carry column resembles like an output of the AND gate.
Inputs |  | Outputs | 
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
S = A ⊕ B
C = AB
A
B

## Slide 4: Limitation of Half-Adder
In multi-digit addition we have to add two bits along with the carry of previous digit addition. Such addition requires addition of 3 bits. This is not possible in half-adders.

## Slide 5: Full Adder
In a full adder, three bits can be added at a time. The third bit is a carry from a less significant column.
Inputs |  |  | Outputs | 
A | B | Cin | S | Cout
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
S = A’B’Cin + A’BCin‘ + AB’Cin’ + ABCin
= (AB’ + A’B)Cin’ + (AB + A’B’)Cin
= (A ⊕ B)Cin’ + (A ⊕ B)’Cin
= A ⊕ B ⊕ Cin
Cout = A’BCin + AB’Cin + ABCin’ + ABCin
= AB + (A ⊕ B)Cin

## Slide 6: Full Adder
Logic diagram for full adder
A
B
Cin
S = A ⊕ B ⊕ Cin
Cout = AB + (A ⊕ B)Cin
Half Adder
Half Adder
S = A ⊕ B ⊕ Cin
Cout = AB + (A ⊕ B)Cin

## Slide 7: Half Subtractor
Subtracts one bit from the other and produces the difference.
Other output is to specify if 1 is borrowed
Inputs |  | Outputs | 
A | B | d | b
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
d = A ⊕ B
b = A’B
A
B

## Slide 8: Full Subtractor
Half subtractor can be used only for LSB subtraction.
Borrow from LSBs affects the subtraction in the next higher column.
Subtrahend bit is subtracted from minuend and consider borrow if generated from preceding column.
Full subtractor is a combinational circuit with 3 inputs (A, B, bi)
Subtraction = A – B – bi

## Slide 9: Full Subtractor
Inputs |  |  | Outputs | 
A | B | bi | d | b
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
d = A’B’bi + A’Bbi‘ + AB’bi’ + ABbi
= (AB’ + A’B)bi’ + (AB + A’B’)bi
= (A ⊕ B)bi’ + (A ⊕ B)’bi
= A ⊕ B ⊕ bi
b = A’B’bi + A’Bbi’ + A’Bbi + ABbi
= A’B(bi + bi’) + (AB + A’B’)bi
= A’B + (A ⊕ B)’bi

## Slide 10: Full Subtractor
A
B
Cin
d = A ⊕ B ⊕ bi
b = A’B + (A ⊕ B)’bi
d = A ⊕ B ⊕ bi
b = A’B + (A ⊕ B)’bi

## Slide 11: Multiplexer
A multiplexer(MUX) is a device that allows digital information from several sources to be routed onto a single line for transmission over that line to a common destination.
Consider an integer ‘m’, which is constrained by the following relation:
m = 2n, where m and n are both integers.
A m-to-1 Multiplexer has
  m Inputs: I0, I1, I2, ................ I(m-1)
  One Output: Y
  n Control inputs: S0, S1, S2, ...... S(n-1)
  One (or more) Enable input(s)
such that Y may be equal to one of the inputs, depending upon the control inputs.

## Slide 12: 4-to-1 Multiplexer
I0
I1
I2
I3
S0
S1
Y
1 output
n control inputs
2n inputs
Enable (G)
4 x 1 MUX
Select Inputs |  | Output
S1 | S0 | Y
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3
Y = S1’S0’I0 + S1’S0I1 + S1S0’I2 + S1S0I3
0
0
I0

## Slide 13: 4 x 1 MUX Actual Circuit
I3
I2
I1
I0
S0
S1
Enable (G)
Y

## Slide 14: Application of Multiplexer
Logic function generation
Data selection
Data routing
Operation sequencing
Parallel-to-serial conversion
Waveform generation

## Slide 15: Logic function generator
Implement the following function using 8 to 1 MUX
F(x,y,z) = Σ m(0,2,3,5)
S2 | S1 | S0 | F
x | y | z | 
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
8 x 1 MUX
D0
D1
D2
D3
D4
D5
D6
D7
S0
S1
S2
z
y
x
1
1
1
1
0
0
0
0
Output = F

## Slide 16: Logic function generator
Multiplexer with n-data select inputs can implement any function of n + 1 variables.
The first n variables of the function as the select inputs and to use the least significant input variable and its complement to drive some of the data inputs.
If the single variable is denoted by D, each data output of the multiplexer will be D, D’, 1, or 0.
Suppose, we wish to implement a 4-variable logic function using a multiplexer with three data select inputs.
Let the input variables be A, B, C, and D; D is the LSB.

## Slide 17: Logic function generator
A truth table for the function F(A, B, C, D) is constructed with ABC has the same value twice once with D = 0 and again with D = 1.
The following rules are used to determine the connections that should be made to the data inputs of the multiplexer.
  If F = 0 both times when the same combination of ABC occurs, connect logic 0 to the data input selected by that combination.
  If F = 1 both times when the same combination of ABC occurs, connect logic 1 to the data input selected by that combination.
  If F is different for the two occurrences of a combination of ABC, and if F = D in each case, connect D to the data input selected by that combination.
  If F is different for the two occurrences of a combination of ABC, and if F = D in each case, connect D to the data input selected by that combination.

## Slide 18
S2 | S1 | S0 | D | F | 
A | B | C |  |  | 
0 0 | 0 0 | 0 0 | 0 1 | 1 1 | F = 1
0 0 | 0 0 | 1 1 | 0 1 | 1 1 | F = 1
0 0 | 1 1 | 0 0 | 0 1 | 1 0 | F = D’
0 0 | 1 1 | 1 1 | 0 1 | 0 0 | F = 0
1 1 | 0 0 | 0 0 | 0 1 | 0 0 | F = 0
1 1 | 0 0 | 1 1 | 0 1 | 1 1 | F = 1
1 1 | 1 1 | 0 0 | 0 1 | 0 0 | F = 0
1 1 | 1 1 | 1 1 | 0 1 | 1 1 | F = 1
Implement the following function using 8 to 1 MUX F = Σ m(0,1,2,3,4,10,11,14,15)
8 x 1 MUX
D0
D1
D2
D3
D4
D5
D6
D7
S0
S1
S2
C
B
A
1
D’
0
1
1
0
0
1
Output = F