## Slide 1: Unit – 4 Flip Flops, Counters and Registers
Hardik Doshi
 99789 11553
 hardik.doshi@darshan.ac.in
Digital Electronics (2131004) Darshan Institute of Engineering & Technology

## Slide 2: Topics to be covered
Types of Flip Flops
Flip Flops and its Applications

## Slide 3: Sequential Switching Circuits
Sequential switching circuits are circuits whose output levels at any instant of time are dependent not only on the levels present at the inputs at that time, but also on the state of the circuit, i.e. on the prior input level conditions (i.e. on its past inputs)
The past history is provided by feedback from the output back to the input.
Made up of combinational circuits and memory elements.
Eg. Counters, shift registers, serial adder, etc.

## Slide 4: Sequential Switching Circuits
Combinational Circuit
Memory elements
Inputs
Outputs

## Slide 5: Sequential Circuits v/s Combinational Circuits
Sequential Circuits
In sequential circuits, the output variables at any instant of time are dependent not only on the present input variables, but also on the present state, i.e. on the past history of the system.
Memory unit is required to store the past history of the input variables in sequential circuits.
Sequential circuits are slower than combinational circuits.
Sequential circuits are comparatively harder to design.
Combinational Circuits
In combinational circuits, the output variables at any instant of time are dependent only on the present input variables.
Memory unit is not required in combinational circuits.
Combinational circuits are faster because the delay between the input and the output is due to propagation delay of gates only.
Combinational circuits are easy to design.

## Slide 6: Flip-flop
A flip-flop, known formally as bistable multivibrator, has two stable states.
It can remain in either of the states indefinitely.
Its state can be changed by applying the proper triggering signal.

## Slide 7: Latch
Latch is used for certain flip-flop which are non-clocked.
These flip-flops ‘latch on’ to a 1 or a 0 immediately upon receiving the input pulse called SET or RESET.

## Slide 8: S-R Flip-Flop (Latch)
The simplest type of flip-flop is called an S-R latch.
It has two outputs labelled Q and Q’ and two inputs labelled S and R. The state of the latch corresponds to the level of Q (HIGH or LOW, 1 or 0) and Q’ is the complement of that state.
It can be constructed using either two cross-coupled NAND gates or two-cross coupled NOR gates.
Using two NOR gates, an active-HIGH S-R latch can be constructed and using two NAND gates an active-LOW S-R latch can be constructed.
The name of the latch, S-R or SET-RESET, is derived from the names of its inputs.

## Slide 9: NOR Gate S-R latch (Active High)
S
R
Q
Q’
Inputs
Outputs
S | R | Qn | Qn+1 | State
0 0 | 0 0 | 0 1 | 0 1 | No Change
0 0 | 1 1 | 0 1 | 0 0 | Reset
1 1 | 0 0 | 0 1 | 1 1 | Set
1 1 | 1 1 | 0 1 | x x | Indeterminate (invalid)
R
S
Q
Q’
Logic diagram
Logic Symbol

## Slide 10: NAND Gate S-R latch (Active Low)
S | R | Qn | Qn+1 | State
0 0 | 0 0 | 0 1 | x x | Indeterminate (invalid)
0 0 | 1 1 | 0 1 | 1 1 | Set
1 1 | 0 0 | 0 1 | 0 0 | Reset
1 1 | 1 1 | 0 1 | 0 1 | No Change
S
R
Q
Q’
Logic diagram

## Slide 11: Gated S-R Latch
S
R
Q
Q’
EN | S | R | Qn | Qn+1 | State
1 1 | 0 0 | 0 0 | 0 1 | 0 1 | No Change
1 1 | 0 0 | 1 1 | 0 1 | 0 0 | Reset
1 1 | 1 1 | 0 0 | 0 1 | 1 1 | Set
1 1 | 1 1 | 1 1 | 0 1 | x x | Indeterminate (invalid)
0 0 | x x | x x | 0 1 | 0 1 | No Change
S
R
Q
Q’
Logic diagram
Logic Symbol
EN
EN

## Slide 12: Gated D-Latch
D
Q
Q’
EN | D | Qn | Qn+1 | State
1 1 | 0 0 | 0 1 | 0 0 | Reset
1 1 | 1 1 | 0 1 | 1 1 | Set
0 0 | x x | 0 1 | 0 1 | No Change
D
Q
Q’
Logic diagram
Logic Symbol
EN
EN

## Slide 13: J-K Flip-Flop
J
K
Q
Q’
Inputs
Outputs
J | K | Qn | Qn+1 | State
0 0 | 0 0 | 0 1 | 0 1 | No Change
0 0 | 1 1 | 0 1 | 0 0 | Reset
1 1 | 0 0 | 0 1 | 1 1 | Set
1 1 | 1 1 | 0 1 | 1 0 | Toggle
K
J
Q
Q’
Logic Symbol
CP
EN

## Slide 14: T Flip-Flop
T
Q
Q’
Inputs
Outputs
T
Q
Q’
Logic Symbol
CP
EN
T | Qn | Qn+1 | State
0 0 | 0 1 | 0 1 | No Change
1 1 | 0 1 | 1 0 | Toggle

## Slide 15: Registers
As a flip-flop (FF) can store only one bit of data, a 0 or a 1, it is referred to as a single-bit register.
A register is a set of FFs used to store binary data.
The storage capacity of a register is the number of bits (1s and 0s) of digital data it can retain.

## Slide 16: Registers
Loading a register means setting or resetting the individual FFs, i.e. inputting data into the register so that their states correspond to the bits of data to be stored.
Loading may be serial or parallel.
In serial loading, data is transferred into the register in serial form i.e. one bit at a time.
In parallel loading, the data is transferred into the register in parallel form meaning that all the FFs are triggered into their new states at the same time.

## Slide 17: Types of Registers
Buffer register
Shift register
Bidirectional shift register
Universal shift register

## Slide 18: 4-bit Buffer Register
FF1
D1
Q1
>
FF2
D2
Q2
>
FF3
D3
Q3
>
FF4
D4
Q4
>
X1
X2
X3
X4
CLK
X4X3X2X1
Q4Q3Q2Q1 =
Q = X
On positive clock edge

## Slide 19: Shift Register
A number of FFs connected together such that data may be shifted into and shifted out of them is called a shift register.
Data may be shifted into or out of the register either in serial form or in parallel form.
So, there are four basic types of shift registers:
  serial-in, serial-out
  serial-in, parallel out
  parallel-in, serial-out
  parallel-in, parallel-out
Data may be rotated left or right. Data may be shifted from left to right or right to left at will, i.e. in a bidirectional way.
Also, data may be shifted in serially (in either way) or in parallel and shifted out serially (in either way) or in parallel.

## Slide 20: Data transmission in shift register
Serial-in, serial-out shift-right, shift register
Serial data input
Serial data output
Serial-in, serial-out shift-left, shift register
Serial data output
Serial data input

## Slide 21: Data transmission in shift register
Serial-in, parallel-out, shift register
Serial data input
Parallel data output
Parallel-in, parallel-out, shift register
Parallel data input
Parallel data output

## Slide 22: Data transmission in shift register
Parallel-in, serial-out, shift register
Serial data output
Parallel data input

## Slide 23: Serial-in, Serial-out, Shift register
FF1
D1
Q1
>
FF2
D2
Q2
>
FF3
D3
Q3
>
FF4
D4
Q4
>
Serial Input
CLK
Serial output

## Slide 24: Serial-in, Serial-out, Shift register
CLK
Serial output
Using J-K Flip Flop
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
FF3
J3
Q3
>
K3
Q3’
FF4
J4
Q4
>
K4
Q4’
Serial input

## Slide 25: Serial-in, Serial-out, Shift-left, Shift register
FF4
Q4
D4
>
FF3
Q3
D3
>
FF2
Q2
D2
>
FF1
Q1
D1
>
Serial Output
CLK
Serial input

## Slide 26: Serial-in, Parallel-out, Shift register
FF1
D1
QA
>
FF2
D2
QB
>
FF3
D3
QC
>
FF4
D4
QD
>
Serial Input
CLK
QA
QB
QC
QD

## Slide 27: Parallel-in, Serial-out, Shift register
FF1
D1
Q1
>
FF2
D2
Q2
>
FF3
D3
Q3
>
FF4
D4
Q4
>
Shift/
CLK
A
B
C
D

## Slide 28: Parallel-in, Parallel-out, Shift register
FF1
D
Q
>
FF2
D
Q
>
FF3
D
Q
>
FF4
D
Q
>
A
CLK
B
C
D
QA
QB
QC
QD

## Slide 29: Bidirectional Shift Register
FF1
D1
Q1
>
FF2
D2
Q2
>
FF3
D3
Q3
>
FF4
D4
Q4
>
Right/
CLK
Din

## Slide 30: Universal Shift Register
4 x 1
MUX4
3 2 1 0
4 x 1
MUX3
3 2 1 0
4 x 1
MUX2
3 2 1 0
4 x 1
MUX1
3 2 1 0
FF4
C
D
^
CLK
FF3
C
D
^
FF2
C
D
^
FF1
C
D
^
A3
A2
A1
A0
s1
s0
I3
I2
I1
I0
Serial input for shift-right
Serial input for shift-left

## Slide 31: Universal Shift Register (Function table)
S1 | S0 | Operation
0 | 0 | No change
0 | 1 | Shift Right
1 | 0 | Shift Left
1 | 1 | Parallel Load

## Slide 32: 2-bit Ripple Up-Counter using Negative Edge-triggered Flip-Flop
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
1
Q1
Q2
CLK
CLK | Present State |  | Next State | 
 | Q2 | Q1 | Q2 | Q1
0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
CLK
Q1
Q2
0
1
0
1
0
0
1
0

## Slide 33: 2-bit Ripple Down-Counter using Negative Edge-triggered Flip-Flop
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
1
Q1
Q2
CLK
CLK | Present State |  | Next State | 
 | Q2 | Q1 | Q2 | Q1
0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0
0 | 1 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0
CLK
Q1
Q2
0
1
0
1
0
0
1
0

## Slide 34: 2-bit Ripple Up-Counter using Positive Edge-triggered Flip-Flop
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
1
Q1
Q2
CLK
CLK | Present State |  | Next State | 
 | Q2 | Q1 | Q2 | Q1
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
CLK
Q1
Q2
0
0
0
1
0
0
1
1
1

## Slide 35: 2-bit Ripple Down-Counter using Positive Edge-triggered Flip-Flop
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
1
Q1
Q2
CLK
CLK | Present State |  | Next State | 
 | Q2 | Q1 | Q2 | Q1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
CLK
Q1
Q2
0
0
0
1
0
0
1
1
1

## Slide 36: Mod-6 Asynchronous Counter
After pulses | State |  |  | Reset(R)
 | Q1 | Q2 | Q3 | 
0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
2 | 0 | 1 | 0 | 0
3 | 0 | 1 | 1 | 0
4 | 1 | 0 | 0 | 0
5 | 1 | 0 | 1 | 0
6 | 1 | 1 | 0 | 1
 | ↓ | ↓ | ↓ | 
 | 0 | 0 | 0 | 0
7 | 0 | 0 | 1 | 0
R = 0 for 000 to 101
R = 1 for 110
R = x for 111
R = Q3Q2Q1’ + Q3Q2Q1
R = Q3Q2

## Slide 37: Mod-6 Asynchronous Counter
FF1
T1
Q1
>
Q1’
FF2
T2
Q2
>
Q2’
FF3
T3
Q3
>
Q3’
1
Q1
Q2
1
1
Q3
R’

## Slide 38: Exercise
Design Mod-10 ripple counter.
Draw a frequency divider using JK FFs to divide input clock frequency by a factor of 8.

## Slide 39: Design of Synchronous Counters
Step 1. Number of flip-flops:
Based on the description of the problem, determine the required number n of the FFs - the smallest value of n is such that the number of states N ≤ 2n and the desired counting sequence.
Step 2. State diagram:
Draw the state diagram showing all the possible states.
Step 3. Choice of flip-flops and excitation table:
Select the type of flip-flops to be used and write the excitation table.
An excitation table is a table that lists the present state (PS), the next state (NS) and the required excitations.

## Slide 40: Design of Synchronous Counters
Step 4. Minimal expressions for excitations:
Obtain the minimal expressions for the excitations of the FFs using K-maps for the excitations of the flip-flops in terms of the present states and inputs.
Step 5. Logic Diagram:
Draw the logic diagram based on the minimal expressions.

## Slide 41: Excitation Tables
PS | NS | Required inputs | 
Qn | Qn+1 | S | R
0 | 0 | 0 | x
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | x | 0
S-R FF
PS | NS | Required inputs | 
Qn | Qn+1 | J | K
0 | 0 | 0 | x
0 | 1 | 1 | x
1 | 0 | x | 1
1 | 1 | x | 0
J-K FF

## Slide 42: Excitation Tables
PS | NS | Required inputs
Qn | Qn+1 | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
D FF
T FF
PS | NS | Required inputs
Qn | Qn+1 | T
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 43: Design of Synchronous 3-bit Up Counters
Step 1. Number of flip-flops:
A 3-bit up-counter requires 3 flip-flops. The counting sequence is 000, 001, 010, 011, 100, 101, 110, 111, 000 …
Step 2. Draw the state diagram:
000
001
010
011
100
101
110
111

## Slide 44: Design of Synchronous 3-bit Up Counters
Step 3. Select the type of flip-flops and draw the excitation table:
JK flip-flops are selected and the excitation table of a 3-bit up-counter using J-K flip-flops is drawn as shown below.
PS |  |  | NS |  |  | Required excitations |  |  |  |  | 
Q3 | Q2 | Q1 | Q3 | Q2 | Q1 | J3 | K3 | J2 | K2 | J1 | K1
0 | 0 | 0 | 0 | 0 | 1 | 0 | x | 0 | x | 1 | x
0 | 0 | 1 | 0 | 1 | 0 | 0 | x | 1 | x | X | 1
0 | 1 | 0 | 0 | 1 | 1 | 0 | x | x | 0 | 1 | x
0 | 1 | 1 | 1 | 0 | 0 | 1 | x | x | 1 | x | 1
1 | 0 | 0 | 1 | 0 | 1 | x | 0 | 0 | x | 1 | x
1 | 0 | 1 | 1 | 1 | 0 | x | 0 | 1 | x | x | 1
1 | 1 | 0 | 1 | 1 | 1 | x | 0 | x | 0 | 1 | x
1 | 1 | 1 | 0 | 0 | 0 | x | 1 | x | 1 | x | 1

## Slide 45: Design of Synchronous 3-bit Up Counters
Step 4. Obtain the minimal expressions
From excitation table, J1 = K1 = 1.
K – Maps for excitations J3, K3, J2 and K2 and their minimized form are as follows:
Q2Q1
Q3
00
10
0
1
01
11
1
x
x
x
x
J3 = Q2Q1
Q2Q1
Q3
00
10
0
1
01
11
1
x
x
x
x
K3 = Q2Q1

## Slide 46: Design of Synchronous 3-bit Up Counters
Q2Q1
Q3
00
10
0
1
01
11
1
x
1
x
J2 = Q1
Q2Q1
Q3
00
10
0
1
01
11
1
x
x
x
x
K2 = Q1
1
x
x

## Slide 47: Design of Synchronous 3-bit Up Counters
Step 5. Draw the logic diagram
FF1
J1
Q1
>
K1
Q1’
FF2
J2
Q2
>
K2
Q2’
1
FF3
J3
Q3
>
K3
Q3’
CLK

## Slide 48: Ring Counter
FF1
D1
Q1
>
FF2
D2
Q2
>
FF3
D3
Q3
>
FF4
D4
Q4
>
CLK
Q1’
Q2’
Q3’
Q4’

## Slide 49: Ring Counter
After pulses | State |  |  | 
 | Q1 | Q2 | Q3 | Q4
0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0
2 | 0 | 0 | 1 | 0
3 | 0 | 0 | 0 | 1
4 | 1 | 0 | 0 | 0
5 | 0 | 1 | 0 | 0
6 | 0 | 0 | 1 | 0
7 | 0 | 0 | 0 | 1