## Slide 1: Unit – 5 Introduction to State Machines
Hardik Doshi
 99789 11553
 hardik.doshi@darshan.ac.in
Digital Electronics (2131004) Darshan Institute of Engineering & Technology

## Slide 2: Topics to be covered
The Need for State Machines
The State Machine
Basic Concepts in State Machine Analysis

## Slide 3: State Machine Definition
A state machine, also called a sequential machine, is a system that can be described in terms of a set of states that the system may enter.
Once in a particular state, the system must be capable of remaining in that state for some finite period of time even if the system inputs change.
This requirement dictates memory capability for the state machine.
Furthermore, the state machine must have a set of inputs and a set of outputs.
As the system progresses from one state to another (from present state to next state), the next state reached depends on the inputs and the present state.
The outputs also depend on inputs and the present state.

## Slide 4: Advantages of Finite State Machine
Many electronic systems require the type of sequential operation exhibited by state machines.
State machine design methods lead to minimal design. The state machine design procedure relates to sequential circuit design in the same way the K-map relates to combinational circuit design. This method results in the minimum number of required flip-flops and can minimize other circuitry in the system as well.
It is a well-developed, orderly procedure that anticipates and solves commonly occurring problems of sequential circuits. State machine methods eliminate the problems of narrow unwanted pulse or glitches on output lines or oscillation problems and reduce the time taken to debug the implemented hardware.

## Slide 5: General Model of Sequential Machine
Input forming logic
(Combinational)
Output forming logic
(Combinational)
Memory
Inputs
Outputs

## Slide 6: General Model of Sequential Machine
This model is also called the Mealy machine.
The input forming logic (IFL) and the output forming logic (OFL) sections are made up of combinational logic circuits.
The memory section contains the state of the system.
A path is provided from memory output to the IFL. Both input signals and present state signals drive the IFL to determine the next state of the system.
The outputs are determined by the present state and the system inputs.
A slight variation of the Mealy machine is the Moore machine, which uses only the memory to drive the OFL. In this case, the output is a function only of the state of the system.

## Slide 7: Types of Finite State Machine
Mealy Model
Moore Model

## Slide 8: 1. Mealy Model
When the output of the sequential circuit depends on both the present state of the flip-flops and on the inputs, the sequential circuit is referred to as Mealy circuit or Mealy machine.
Input forming logic
(Combinational)
Output forming logic
(Combinational)
Memory
Inputs
Outputs

## Slide 9: Logic Diagram of Mealy Model
D1
y1
y1’
D2
y2
y2’
x
z

## Slide 10: 1. Mealy Model
y1(t+1) = y1(t) x(t) + y2(t) x(t)
y2(t+1) = y1’(t) x(t)
z(t) = {y1(t) + y2(t)} x’(t)
y1(t+1) = Y1 = y1 x + y2 x
y2(t+1) = Y2 = y1’ x
z = (y1 + y2) x’
Considering Y1(t) & Y2(t) for y1(t+1) & y2(t+1) respectively
State Equations

## Slide 11: 1. Mealy Model
PS |  | NS |  |  |  | O/P | 
 |  | x = 0 |  | x = 1 |  | x = 0 | x = 1
y1 | y2 | Y1 | Y2 | Y1 | Y2 | z | z
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
State Table

## Slide 12: 2. Moore Model
When the output of the sequential circuit depends only on the present state of the flip-flop, the sequential circuit is referred to as Moore circuit or the Moore machine.
Input forming logic
(Combinational)
Output forming logic
(Combinational)
Memory
Inputs
Outputs

## Slide 13: Logic Diagram of Moore Model
T1
y1
y1’
T2
y2
y2’
x
z
CLK
>
>

## Slide 14: 2. Moore Model
T1 = y2 x
z = y1 y2
Q(t+1) = TQ’ + T’Q = T ⊕ Q
y1(t+1) = Y1 = (y2x) ⊕ y1 = (y2x)’ y1 + y1’y2x = y1y2’ + y1x’ + y1’y2x
Input & Output Equations
T2 = x
Characteristic equation of T Flip-Flop
State Equations
y2(t+1) = Y2 = x ⊕ y2 = xy2’ + x’y2

## Slide 15: 2. Moore Model
PS |  | NS |  |  |  | O/P
 |  | x = 0 |  | x = 1 |  | 
y1 | y2 | Y1 | Y2 | Y1 | Y2 | z
0 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 1 | 1 | 0
1 | 1 | 1 | 1 | 0 | 0 | 1
State Table