## Slide 1: Unit – 8 Logic Families
Hardik Doshi
 99789 11553
 hardik.doshi@darshan.ac.in
Digital Electronics (2131004) Darshan Institute of Engineering & Technology

## Slide 2: Topics to be covered
Transistor-Transistor Logic(TTL)
Emitter-Coupled Logic(ECL)
CMOS Logic

## Slide 3: Digital IC Specification
Threshold voltage
Propagation Delay
Power dissipation
Fan-in
Fan-out
Voltage & Current parameters
Noise Margin
Operating Temperatures
Speed power products

## Slide 4: TTL v/s CMOS v/s ECL
Characteristic | TTL | CMOS | ECL
Power Input | Moderate | Low | Moderate-High
Frequency limit | High | Moderate | Very high
Circuit density | Moderate-high | High-very high | Moderate
Circuit types per family | High | High | Moderate
Logic Family | Propagation delay time (ns) | Power dissipation per gate (mW) | Noise Margin (V) | Fan-in | Fan-out | Cost
TTL | 9 | 10 | 0.4 | 8 | 10 | Low
CMOS | <50 | 0.01 | 5 | 10 | 50 | Low
ECL | 1 | 50 | 0.25 | 5 | 10 | High