## Slide 1
Name: Mistry Mihir R
En.No.:160410116061
Sub.: DE
Emitter coupled logic,VEM

## Slide 2: Emitter Coupled Logic:
The basic circuit of the ECL family is the NOR gate.
The special advantage of ECL gate is their low propagation delay.
ECL version may have a propagation delay as low as 0.5 ns.

## Slide 3
The power dissipation in ECL gates is comparatively high and the noise margin low.
These two parameters impose a disadvantage when choosing ECL over other logic families.
However, because of its low propagation delay, ECL offers the highest speed of any family and is the ultimate choice for very fast systems.

## Slide 4
The most common ECL type is designated as the 10,000 series.
The 10102 provides four 2-input NOR gates.
An ECL gate may have two outputs, one for the NOR function and another for the OR function.
The 10107 IC provides three exclusive-OR gates.

## Slide 5
There are two output from the each gate ; the other output gives the supply.
Vcc1 and Vcc2 are usually connected to ground , and VEE to a -5.2-volt supply.

## Slide 6: Variable Entered Map:
A variable entered map (VEM) is a Karnaugh map in which the size of the map is reduced by removing one or more of the variables from the specification of the map cell locations.
Instead of having only the 1's and 0's in the cells of the original map, the cells of the VEM contain functions of the variables which were removed.

## Slide 7
Consider a function of four variables, A, B, C, and D. The Karnaugh map will have 16 cells each containing a 1 or a 0.
Note that 1 and 0 are the only two possible functions of zero variables, and each cell must contain one of these functions since all variables are used to define the cell locations.

## Slide 8
If the map is reduced to three variables, A, B, and C for example, then the resulting variable entered map will have 8 cells with locations identified by A, B, and C.
The contents of each cell will be one of the four possible functions of the variable D.

## Slide 9
Those four functions are 1, 0, D, and D'.
If the map is reduced to two variables, A and B or example, then the map will have four cells, and each cell will contain one of the 16 possible functions of C and D.
This representation is useful for representing function of four or more variables when there is a simplifying structure of variable dependence.

## Slide 10
For example, consider a 4 to 1 MUX with select inputs S1 and S0 and data inputs D0, D1, D2, and D3.
This would require a 64 cell K-map to represent the function of 6 variables.
However, in this case a variable entered map of two variables, S1 and S0 has the corresponding data input in each cell.

## Slide 11
This is easily demonstrated with a 2 to 1 MUX with output Y given by Y=S0'(D0) + S0(D1) which can be represented with an 8 cell K-map.
A two cell VEM also represents this function in a simple form and has the advantage of making the function of the circuit more obvious.

## Slide 12
Conversely, the inputs to a MUX used to implement an arbitrary logic function can be determined by using a variable entered map.
The select variables for the MUX are the variables which determine the locations of the cells of the map, and functions of the remaining variables define the cell contents, which are the MUX data inputs.

## Slide 13: Thank You